## Slide 1: PAWS Navigation: Reinforcement Learning for Path Planning in Unknown Environments
Samantha Johnson
University of Maryland, College Park
ENPM690 – Robot Learning

## Slide 2: PAWS (Psychological Assistance and Wellness System)
“Hypothetical” robot that has been researched and designed over graduate education
In-home mental health robotic pet companion
Navigation is a crucial component
  Needs to quickly navigate to the human’s location and avoid obstacles
  The environment is unknown

## Slide 3: Machine Learning and Path Planning
Path planning in unknown environments is not a capability common to most path planning algorithms
  Most require a map of the area in order to effectively plan
Introducing machine learning can help mitigate the need for a map
Research with promising results using reinforcement learning showing ability to navigate unknown/dynamic terrain and reach a goal
  Able to find semi-optimal paths

## Slide 4: Algorithm
Utilizing a type of reinforcement learning called Double Deep Q-Network (DDQN)
Features:
  Epsilon Greedy Strategy to promote exploration early in the training phase
  Experience Replay to reduce correlation between training batches
  Target Network to calculate target values and improve estimate
Goals:
  Train robot to navigate to a changing goal in an unknown environment
  Avoid obstacles
  Find a timely path

## Slide 5: Algorithm
Initialize the environment and agent
Copy the policy network to the target network
For each episode:
  Initialize the simulation
  For each time in max time:
    Select an action based on e-greedy strategy
      Random or from neural net
    Execute action in simulation environment
    Return reward obtained and next state
    Store last experience in replay memory
    Perform neural net training
      Select batch of memories to replay through policy network
      Utilize the target net to obtain values for the next state
      Calculate the loss between the output Q values and target Q values
      Gradient descent to minimize loss
    Decay epsilon
    After a set time update the target net weights to match the policy net weights
https://deeplizard.com/learn/video/0bt0SjbS3xc

## Slide 6: Technologies
CoppeliaSim – simulation software
Python - algorithm
  Interfacing with CoppeliaSim via the Remote API
  Keras and TensorFlow
  Numpy
  SciPy

## Slide 7: Design
Reward function
  Large reward for reaching goal
  Moderate negative reward for hitting obstacle
  Free space reward
    Positive value for moving towards the objective
    Higher value being near the objective
    Negative value that increases as time passes
State
  0 or 1 for detection by proximity sensor
  Binned vector between the robot and goal
  Normalized time elapsed
Actions
  N
  S
  E
  W

## Slide 8: Simulation environment
CoppeliaSim was used as the simulation software
Environment was designed as a planar area containing:
  Walls and obstacles
  Human marking goal location
Robot was designed as a 2-wheeled mobile robot
  4 proximity sensors pointing [N S E W]
  Motion constrained to [N S E W] directions

## Slide 9: Training
Parameters
Data collection
Distance vs. Time
Error vs. Time
Time vs. Episode
Reward vs. Episode

## Slide 10: Training Difficulties
CoppeliaSim took several hours to run a couple dozen episodes
  ~1 hour per 10 episodes
Physics anomalies during reset caused robot to flip upside down
  Random and would cause training to stop
  Took a long time to observe this happening
Tried to resolve issues via code, but there was little that could be done. Training large numbers of episodes became impossible using this simulation system

## Slide 11: Testing
Tested on max episodes able to train which was 40 episodes
Behavior resulted in going in circles around the central point

## Slide 13: Another approach – Open AI Gym
Implemented Gym as the simulation software instead
Utilized a third-party maze environment called gym-maze
Used originally developed DDQN algorithm
  State of Robot is [X, Y] – different from original state
  Action Space is [N, S, E, W] – same as original actions
  Implemented original reward function (overwriting the one produced by the sim)
https://github.com/MattChanTK/gym-maze

## Slide 14: Testing – open ai gym
Trained 1000 Episodes with a Time Limit of 250
50 % Success rate

## Slide 15: Conclusions
CoppeliaSim was a bad choice for the training environment
  Too long too complete steps
  Dynamics makes it hard to reset environment
State space may have been too large for reasonable training time
  Binning the distance vector helped to emulate grids, but there were still a lot of possible states
Reward function was successful during training in the Gym environment
  Promising result for further work
Future work to implement the intended environment in Gym to allow for 10K+ trainings which should help the original solution converge

## Slide 16: sources
Lei, X., Zhang, Z. & Dong, P. Dynamic Path Planning of Unknown Environment Based on Deep Reinforcement Learning. Journal of Robotics 2018, 1–10 (2018).